Urban Acoustics
Week 6	Tutorial
Cnossos model
prof.dr.ir. Maarten Hornikx
dr. Matthias Cosnefroy

---
Cnossos
Problem :
A residential area is located close to a highway. The façade of the closest house is 110m from the center of the highway. The road has a total vehicle flow of 4000 vehicles per hour which is composed out of 90 % lightweight and 10 % heavy duty vehicles. The lightweight vehicles have a speed of 120 km/h and the heavy duty vehicles a speed of 80 km/h. For the source, a height of 0 m can be used. The ground between the road and the residential area is of the type compacted lawn and the highway asphalt type ‘very hard and dense’. We consider the highway as a line source and the speed of sound is 340 m/s.
a) Compute the sound power LW,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power LW,eq,i for the vehicles together.
7S0X0
2017/02/09
PAGE

---
Cnossos_clipboard2
a) Compute the sound power LW,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power LW,eq,i for the vehicles together.
Answer:
For both the lightweight vehicles (m=1) and the heavy vehicles (m=3), we first use the next formulae to compute the sound power from rolling noise (LWR,i,m) and propulsion noise (LWP,i,m) emitted by one vehicle, for each octave band:
You just have to find the coefficients associated with each vehicle type (for each octave band)

---
Cnossos_clipboard1
a) Compute the sound power LW,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power LW,eq,i for the vehicles together.
For light vehicles, use v1 = 120 km/h, vref = 70 km/h, ΔLWR,i,1 = 0
For heavy vehicles, use v2 = 80 km/h, vref = 70 km/h, ΔLWR,i,2 = 0

---
a) Compute the sound power LW,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power LW,eq,i for the vehicles together.
Once you know the sound power from rolling noise LWR,i,m and propulsion noise LWP,i,m for each octave band and each vehicle type, compute the total sound power per vehicle (logarithmic sum):
You can then compute the sound power per meter associated with the flow of type-m vehicles as
With Q1 = 3600 light vehicles per hour
  and Q3 = 400 heavy vehicles per hour
L_{ W,i,m } =10 {log} rsub {10} left ( {10} ^ {{𝐿} rsub {WR,i,m} over {10}} + {10} ^ {{𝐿} rsub {italic "WP",i,m} over {10}}right )
L_{ W,eq,i,m } =L rsub {W,i,m} + 10 {log} rsub {10} left ( {Q_m} over {1000 v_m} right )

---
a) Compute the sound power Lw,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power Lw,eq,i for the vehicles together.
 Total sound power of light (m=1) and heavy duty (m=3) vehicles per octave band:
f	LWR,i,1	LWP,i,1	LW,i,1	LW,eq,i,1		LWR,i,3	LWP,i,3	LW,i,3	LW,eq,i,3
(Hz)	(dB)	(dB)	(dB)	(dB)		(dB)	(dB)	(dB)	(dB)
63	86.7	93,6	94,4	79,2		88,7	104,4	104,5	81,5
125	95.4	94,3	97,9	82,7		93,6	101,0	101,8	78,7
250	93.6	93,5	96,6	81,3		95,9	102,4	103,2	80,2
500	96.2	91,6	97,5	82,3		102,2	101,7	105,0	81,9
1000	104.9	89,9	105,0	89,8		102,6	100,8	104,8	81,8
2000	102.6	92,6	103,0	87,8		96,5	96,6	99,5	76,5
4000	93.2	89,0	94,6	79,4		89,3	92,0	93,9	70,9

---
a) Compute the sound power Lw,eq,i,m of the highway for the 1/1 octave band range 63-4000 Hz, per vehicle type. Also, compute the total sound power Lw,eq,i for the vehicles together.
    To get the total sound power LW,eq,i for the vehicles together, compute the logarithmic sum of the sound powers per meter:
f	LW,eq,i
(Hz)	(dB)
63	83.5
125	84.2
250	83.8
500	85.1
1000	90.5
2000	88.1
4000	80.0

---
Cnossos_clipboard0
b) Compute the noise level per 1/1 octave band Lp,i at the closest façade due to the highway, at a height of 4 m. Make use of figure 1 for computing the ground effect and Adiv = 10log10(d)+8.
"source-receiver distance" d = sqrt{ 4^2 + 110^2 } approx 110.1 "m"
Sound power LW,eq,i , we know this as we computed it for last question
Attenuation due to geometrical spreading; here, for a line source,
Adiv = 10log10(d)+8 = 28.4 dB (frequency-independent)
Atmospheric absorption Aatm,i = αi d/1000 dB , compute with αi from table below
Attenuation due to ground Aground,i , see next slides
Attenuation due to diffraction: Adif,i = 0 dB (no barrier)
L_{p,i} = L_{W,eq,i} -A_{"div"} -A_{atm,i} -A_{ground,i} -A_{dif,i}

---
Cnossos_clipboard3
b) Compute the noise level per 1/1 octave band Lp,i at the closest façade due to the highway, at a height of 4 m. Make use of figure 1 for computing the ground effect and Adiv = 10log10(d)+8.
Calculation of Aground,i:
Step 1: compute Gs and Gpath based on tabulated values
Ground near the source = dense asphalt, so Gs = 0
Ground along propagation path = compacted lawn only, so Gpath = 0.7
Note: if several ground types are present along the propagation path, you need to compute the weighted average of Gpath .
L_{p,i} = L_{W,eq,i} -A_{"div"} -A_{atm,i} -A_{ground,i} -A_{dif,i}

---
Cnossos_clipboard4
b) Compute the noise level per 1/1 octave band Lp,i at the closest façade due to the highway, at a height of 4 m. Make use of figure 1 for computing the ground effect and Adiv = 10log10(d)+8.
Step 2: compute G’path with the formula
Here, dp = 110 m, zs = 0 m and zr = 4 m, so the condition
is true.
We find
G'_{path} approx 0.6

---
b) Compute the noise level per 1/1 octave band Lp,i at the closest façade due to the highway, at a height of 4 m. Make use of figure 1 for computing the ground effect and Adiv = 10log10(d)+8.
Step 3: from the computed value of G’path , you can estimate Aground,i from the provided figure, for each octave band:
f	Aground,i
(Hz)	(dB)
63	-1.5
125	-1.5
250	-1.5
500	-1.5
1000	-1.5
2000	4.5
4000	8.5
L_{p,i} = L_{W,eq,i} -A_{"div"} -A_{atm,i} -A_{ground,i} -A_{dif,i}

---
b) Compute the noise level per 1/1 octave band Lp,i at the closest façade due to the highway, at a height of 4 m. Make use of figure 1 for computing the ground effect and Adiv = 10log10(d)+8.
You can now compute the noise level per octave band:
f	LW,eq,i	Adiv	Aatm	Agrnd	Adif	Lp,i
(Hz)	(dB)	(dB)	(dB)	(dB)	(dB)	(dB)
63	83,5	28.4	0,0	-1.5	0.0	56,6
125	84,2	28.4	0,0	-1.5	0.0	57,2
250	83,8	28.4	0,1	-1.5	0.0	56,8
500	85,1	28.4	0,3	-1.5	0.0	58,0
1000	90,5	28.4	0,4	-1.5	0.0	63,1
2000	88,1	28.4	1,0	4.5	0.0	54,2
4000	80,0	28.4	2,9	8.5	0.0	40,1
L_{p,i} = L_{W,eq,i} -A_{"div"} -A_{atm,i} -A_{ground,i} -A_{dif,i}

---
c) For the same receiver point as b), compute the A-weighted sound level Lp,A.
Apply the A correction to each octave band, then compute the logarithmic sum of the noise levels:
F (Hz)	63	125	250	500	1KHz	2KHz	4KHz
A-weighting correction factor (dB)	-26.2	-16.1	-8.6	-3.2	0	1.2	1
We find Lp,A = 64.4 dB(A)

---
d) In winter time, the ground between the residential area and the road is occasionally covered by snow. How much does the A-weighted sound level Lp,A change due to this?
With snow the ground absorption will change, so you need to recompute Aground,i :
Now, Gpath=1, leading to G’path = 0.9
You can thus estimate Aground,i from the figure.
Following the same procedure as before, we find Lp,A = 60.0 dB(A),
i.e., a reduction of 4.3 dB(A).

---
e) To reduce the noise level, a thin 4 m tall barrier is erected at 10 m from the road. At the receiver point of b), compute the reduction in A-weighted sound level Lp,A due to the barrier. Make use of figure 2 for this purpose.
Now, absorption due to diffraction:
Here, Aground,i = 0 since the ground effect is already included in Adif,i .
Otherwise, the other terms are the same as before.
Let’s now compute the different terms appearing in the definition of Adif,i ,
accounting for diffraction and the ground effects on both sides of the barrier,
respectively.
L_{p,i} = L_{W,eq,i} -A_{"div"} -A_{atm,i} -A_{ground,i} -A_{dif,i}
A_{dif,i} = %DELTA_{dif,SR,i} + %DELTA_{ground,SO,i} + %DELTA_{ground,italic "OR",i}

---
e) To reduce the noise level, a thin 4 m tall barrier is erected at 10 m from the road. At the receiver point of b), compute the reduction in A-weighted sound level Lp,A due to the barrier. Make use of figure 2 for this purpose.
fm= central frequency of frequency band
h0= height of the barrier

---
e) To reduce the noise level, a thin 4 m tall barrier is erected at 10 m from the road. At the receiver point of b), compute the reduction in A-weighted sound level Lp,A due to the barrier. Make use of figure 2 for this purpose.
See the Matlab script for more details on how to compute these two terms

---
e) To reduce the noise level, a thin 4 m tall barrier is erected at 10 m from the road. At the receiver point of b), compute the reduction in A-weighted sound level Lp,A due to the barrier. Make use of figure 2 for this purpose.
Once you know the new Adif ,
recompute the
A-weighted sound level:
f	LW,eq,i	Adiv	Aatm	Aground	Adif	Lp,i
(Hz)	(dB)	(dB)	(dB)	(dB)	(dB)	(dB)
63	84,1	28.4	0,0	0	5,3	49,8
125	84,2	28.4	0,0	0	7,6	48,1
250	83,8	28.4	0,1	0	9,9	45,3
500	85,1	28.4	0,3	0	12,7	43,8
1000	90,5	28.4	0,4	0	15,5	46,0
2000	88,1	28.4	1,0	0	18,5	40,2
4000	80,0	28.4	2,9	0	21,3	27,3
Lp,A = 48.6 dB(A)

---
f) To even further reduce the noise level, it has been suggested to reduce the speed limit to 100 km/h for the lightweight vehicles. How much would the A-weighted sound level Lp,A reduce due to this measure?
Answer: Reducing the speed reduces the sound power level LW,eq,i,m for the lightweight vehicles. Re-calculate the sound power, then as before compute the sound level Lp,i , then compute the A-weighted sound level.
	without speed limit	with speed limit
no snow, no barrier	64.4	63.0
snow, no barrier	60.0	58.7
no snow, barrier	48.6	47.3
A-weighted sound levels (in dB(A)) for the different configurations, with and without the speed limit
Here, reducing the speed limit decreases the noise by more than 1 dB(A),
although the decrease is rather small compared to the barrier.

---
Questions?
m.h.r.cosnefroy@tue.nl
(last chance!)
7S0X0 / 7W8X0