Urban Physics, 7S0X0

Urban Acoustics, Exercises week 7

This exercise is the continuation of the exercise of week 6. Without the noise barrier, the noise level per 1/1 octave band Lp,i at 110 m from the highway, at a height of 4 m is shown in Table 1.

1. There is a plan to construct an open car-parking space of 10 m width just in front of the residential area. Before it could be built, the planners want to check if the parking ground will lead to an increase in sound levels at the nearest façade; if it does increase, they plan to build the parking space on the other side. Compute the difference in A-weighted sound level Lp,A .
2. For the receiver position at 110 m from the highway and 4 m height, compute the difference in A-weighted sound level Lp,A for favourable conditions. Make use of figure 1 for computing the ground effect and make use of Adiv = 10log10(d)+8, with d the direct distance between source and receiver.
3. To reduce the noise level, a thin 4 m tall barrier was proposed at 10 m from the road. For homogeneous conditions, the values of Lp,i at the receiver point of a) per 1/1 octave band are shown in Table 1. For the same configuration, compute the difference in A-weighted sound level Lp,A for favourable conditions using figure 2.
4. A barrier is also located at 10 m at the other side of the road, see figure 3. Draw the sound rays in figure 3 that determine the sound level at receiver position R due to source position S. Neglect multiple (more than 1) reflections from the noise barrier.
5. Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient α from the barrier is equal to 0. Make use of Figure 4.
6. How much is Lp,A reduced when the faces of the barriers have an absorption coefficient α= 0.9 for all frequencies?

 Table 1. Sound pressure level Lp,i at 110 m from the highway, at a height of 4.

f / (Hz)	Lp,i homogeneous, no barrier	Lp,i / homogeneous / barrier
	(dB)	(dB)
63	56.6	49.8
125	57.2	48.1
250	56.8	45.3
500	58.0	43.8
1000	63.1	46.0
2000	54.2	40.2
4000	40.1	27.3

Figure 1. Aground for various values of G’path for favourable conditions. Lines for G’path = 0 (lowermost line) to G’path = 1 (upper line). Other lines with increment of G’path = 0.2.
Figure 2. Aground for various values of G’path for favourable conditions. Lines for G’path = 0 (lowermost line) to G’path = 1 (upper line). Other lines with increment of G’path = 0.2.

Figure 3. Schematic situation with two noise barriers. The source is located 10 m from each barrier, and the ground in-between the barriers is very hard and dense asphalt (G=0).

Figure 4. Aground for various values of G’path. Lines for G’path = 0 (lowermost line) to G’path = 1 (upper line). Other lines with increment of G’path = 0.2.