Urban Acoustics
Week 7	Tutorial
Cnossos model
prof.dr.ir. Maarten Hornikx
dr. Matthias Cosnefroy

---
Cnossos
Problem:
A residential area is located close to a highway. The façade of the closest house is 110 m from the center of the highway. The road has a total vehicle flow of 4000 vehicles per hour which is composed out of 90% lightweight and 10% heavy duty vehicles. The lightweight vehicles have a speed of 120 km/h and the heavy duty vehicles a speed of 80 km/h. For the source, a height of 0 m can be used. The ground between the road and the residential area is of the type compacted lawn and the highway asphalt type ‘very hard and dense’. We consider the highway as a line source and the speed of sound is 340 m/s.
7S0X0
2017/02/09
PAGE

---
This exercise is the continuation of the exercise of week 6. The noise level per 1/1 octave band Lp,i at 110 m from the highway, at a height of 4 m, is shown in the table below for homogeneous conditions (i.e., without wind) with and without the noise barrier.
F (Hz)	Lp,i / homogeneous, / no barrier (dB)	Lp,i / homogeneous, / barrier (dB)
63	56.6	49.8
125	57.2	48.1
250	56.8	45.3
500	58.0	43.8
1000	63.1	46.0
2000	54.2	40.2
4000	40.1	27.3

---
Cnossos_clipboard0
a) There is a plan to construct an open car-parking space of 10 m width just in front of the residential area. Before it could be built, the planners want to check if the parking ground will lead to an increase in sound levels at the nearest façade; if it does increase, they plan to build the parking space on the other side. Compute, without the barrier, the difference in A-weighted sound level Lp,A.
The terms LW,eq,i , Adiv and Aatm,i are the same as before (without the barrier). Aground,i will change due to the car-parking space though.
Again, 3 steps to compute the ground attenuation:
compute Gs and Gpath based on tabulated values of ground properties
compute G’path with the formula from the lecture
estimate Aground,i from the provided figure, for each octave band
L_{p,i} = L_{W,eq,i} -A_{italic "div"} -A_{atm,i} -A_{ground,i}

---
Cnossos_clipboard1
a) There is a plan to construct an open car-parking space of 10 m width just in front of the residential area. Before it could be built, the planners want to check if the parking ground will lead to an increase in sound levels at the nearest façade; if it does increase, they plan to build the parking space on the other side. Compute, without the barrier, the difference in A-weighted sound level Lp,A.
As before, ground near the source = dense asphalt, so Gs = 0
The ground along the propagation path now consists of 100 m of compacted lawn (G = 0.7) and 10 m of “car park” (G = 0.3)
You thus need to compute Gpath as the average G over the propagation path, i.e: Gpath= (0.7 x 100 + 0.3 x 10) / 110 ≈ 0.66
Note: you could have included the road near the source for computing Gpath , although the difference would have been small since the width of the road is small compared with the total path length (and in any case the influence of the ground near the source is somewhat taken into account via Gs).
2017/03/23

---
Cnossos_clipboard4
a) There is a plan to construct an open car-parking space of 10 m width just in front of the residential area. Before it could be built, the planners want to check if the parking ground will lead to an increase in sound levels at the nearest façade; if it does increase, they plan to build the parking space on the other side. Compute, without the barrier, the difference in A-weighted sound level Lp,A.
Now you can compute G’path with the formula
with dp = 110 m, zs = 0 m and zr = 4 m. We find .
From Figure 1, you can finally (roughly) estimate Aground,i
G'_{path} approx 0.6

---
a) There is a plan to construct an open car-parking space of 10 m width just in front of the residential area. Before it could be built, the planners want to check if the parking ground will lead to an increase in sound levels at the nearest façade; if it does increase, they plan to build the parking space on the other side. Compute, without the barrier, the difference in A-weighted sound level Lp,A.
Next, compute the sound level per octave band and apply the A correction
f	LW,eq,i	Adiv	Aatm	Aground	Adif	Lp,i,old	Lp,i,new
63	83.5	28.4	0.0	-1.7	0.0	56.6	56,8
125	84.2	28.4	0.0	-1.7	0.0	57,2	57,4
250	83.8	28.4	0.1	-1.7	0.0	56.8	57,0
500	85.1	28.4	0.3	-1.7	0.0	58.0	58,2
1000	90.5	28.4	0.4	-1.7	0.0	63.1	63,3
2000	88.1	28.4	1.0	4.3	0.0	54.2	54,4
4000	80.0	28.4	2.9	1.0	0.0	40.1	47.6
Lp,A,old = 64.4 dB(A)
Lp,A,new = 64.7 dB(A)
Slight amplification, but in principle the car park should go to the other side
(but you could also consider that the difference is smaller than
the uncertainty of the Cnossos model...)

---
b) For the receiver position at 110 m from the highway and 4 m height, compute the difference in A-weighted sound level Lp,A for favourable conditions. Make use of figure 1 for computing the ground effect and make us of Adiv = 10log10(d)+8, with d the direct distance between source and receiver.
For favorable conditions, the sound level (for one acoustic path) is expressed as
Aboundary,F,i is either Aground,F,i or Adif,F,i . Here, there is no barrier so
Note: since the other terms are the same as for homogeneous conditions, you can consider the sound level difference between the homogeneous Lp,H,i and the favorable Lp,F,i conditions to avoid recomputing all the terms:
L_{ p,F,i } = L_{ W,i } -A_{italic "div" } -A_{ atm,i } -A_{ boundary,F,i }
L_{ p,F,i } = L_{ W,i } -A_{italic "div" } -A_{ atm,i } -A_{ground,F,i}
L_{ p,F,i } = L_{ p,H,i } +A_{ ground,H,i } -A_{ ground,F,i }

---
b) For the receiver position at 110 m from the highway and 4 m height, compute the difference in A-weighted sound level Lp,A for favourable conditions. Make use of figure 1 for computing the ground effect and make us of Adiv = 10log10(d)+8, with d the direct distance between source and receiver.
Computation of Aground,F,i :
The procedure is exactly the same as for the homogeneous case:
- compute Gpath and Gs
- apply the correction G’path with the same formula
- then use the provided figure to estimate Aground,F,i
(the figure is of course not the same as for the homogeneous case)

---
Aground for various values of G’path for favourable conditions. Lines for G’path = 0 (lowermost line) to G’path = 1 (upper line). Other lines with increment of G’path = 0.2.
Here, G’path≈ 0.64 (without the parking from question a)).
You can then estimate Aground,F,i and compute the sound level with favorable conditions.

---
L_{ p,F,i } = L_{ p,H,i } +A_{ ground,H,i } -A_{ ground,F,i }
f (Hz)	Lp,H,i (dB)	Aground,H,i (dB)	Aground,F,i (dB)	Lp,F,i (dB)
63	56.6	-1,5	-1	56,1
125	57,2	-1,5	-1	56,7
250	56,8	-1,5	-1	56,3
500	58,0	-1,5	-1	57,5
1000	63,1	-1,5	-1	62,6
2000	54,2	4,5	5	53,7
4000	40,1	8,5	0.5	48,1
A-weighted sound level is now Lp,F,A = 64.1 dB(A) (for homogeneous case, it was Lp,H,A = 64.4 dB(A))
This is counter intuitive because one would expect an amplification with favorable conditions:
this is because a favorable wind emphasizes the ground effects

---
c) To reduce the noise level, a thin 4 m tall barrier was proposed at 10 m from the road. For homogeneous conditions, the values of Lp,H,i at the receiver point of a) per 1/1 octave band are shown in Table 1. For the same position, compute the difference in A‐weighted sound level Lp,F,A for favourable conditions using figure 2.
L_{ p,F,i } = L_{ W,i } -A_{italic "div" } -A_{ atm,i } -A_{ boundary,F,i }
Answer:
In favorable conditions with a barrier, we can use the formula
L_{ p,F,i } = L_{ W,i } -A_{italic "div",n } -A_{ atm,i } -A_{ dif,F,i }
As for the previous question, we can also more conveniently compute the difference with the homogeneous case, i.e.,
To compute Adif,F,i use the following formulae
L_{ p,F,i } = L_{ p,H,i } +A_{ dif,H,i } -A_{ dif,F,i }

---
c) To reduce the noise level, a thin 4 m tall barrier was proposed at 10 m from the road. For homogeneous conditions, the values of Lp,H,i at the receiver point of a) per 1/1 octave band are shown in Table 1. For the same position, compute the difference in A‐weighted sound level Lp,F,A for favourable conditions using figure 2.
With homogeneous conditions:	With favorable conditions:
A_{dif,H,i} = %DELTA_{dif,SR,i} + %DELTA_{ground,SO,i} + %DELTA_{ground,italic "OR",i}
A_{dif,F,i} = %DELTA_{dif, widehat {SR} ,i} + %DELTA_{ground, widehat {SO} ,i} + %DELTA_{ground,italic widehat {"OR"} ,i}

---
Cnossos_clipboard2

---
Check out the provided Matlab script for the details of the computations!

---
L_{ p,F,i } = L_{ p,H,i } +A_{ dif,H,i } -A_{ dif,F,i }
f (Hz)	Lp,H,i (dB)	Adif,H,i (dB)	Adif,F,i (dB)	Lp,F,i (dB)
63	49,8	5,3	5,2	49,9
125	48,1	7,6	7,5	48,2
250	45,3	9.9	9,8	45,5
500	43,8	12,7	12,5	43,9
1000	46,0	15,5	15,4	46,2
2000	40,2	18,5	18,3	40.4
4000	27,3	21,1	21.2	27,4
A-weighted sound level is a bit larger and is now Lp,F,A = 48.8 dB(A)
        for homogeneous case, it was Lp,H,A = 48.6 dB(A)
Here, the difference is small because the source is very close to the barrier.
So the barrier is effective even in favorable conditions.

---
Cnossos_clipboard3
d) A barrier is also located at the other side of the road, see figure 3. Draw the sound rays in figure 3 that determine the sound level at receiver position R due to source position S. Neglect multiple (more than 1) reflections from the noise barrier.
Path 1
O’
O
Path 2
O
O’
S
R
S’
S
R

---
Cnossos_clipboard5
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
To compute Lp,A , we need to compute the sound levels associated with each path, Lp,n=1,i and Lp,n=2,i . We already know the level associated with path 1 thanks to the exercises of week 6, so we only need to compute Lp,n=2,i , with
Because of the reflection on the second barrier, we consider the image-source S’ as the source for path 2
This means that we “remove” the second barrier, so we just have to consider the diffraction on the first barrier. The problem thus becomes very similar to the exercise of week 6.
L_{ p,2,i } = L_{ W',i } -A_{italic "div",2}(S'R) -A_{ atm,2,i}(S'R) -A_{ boundary,2,i }

---
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
LW’,2,i is the sound power of the virtual source S’, defined as
This corresponds to the sound power of the original source LW,2,i , with a correction factor to account for the absorption of the barrier αr,i , and a correction factor to account for retrodiffraction:
with δ’ = S’O – SO’ – OO’ .
Note: here, there is also a diffraction due to the first barrier, so you must consider the path between the image-source S’ and the diffraction point O, at the top of the first barrier (see previous figure), and not the actual receiver R,
to compute δ’ (see Cnossos report, page 98).
L_{W',i} = L_{W,i} + 10 "log"_10 (1-%alpha_{r,i})-%DELTA_{retrodif,i}
%DELTA_{retrodif,i}

---
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
Computing Adiv,2 and Aatm,2,i is the same as before, except that you need to consider the path length S’R instead of SR:
Adiv,2 = 10 log10(S’R)+8 (because the road is considered as a line source)
Aatm,2,i = αi S’R/1000 dB (the coefficients αi are tabulated, see previous tutorials)

---
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
To compute Aboundary,2,i , use the same procedure as in tutorial of week 6 with the barrier, except that the source position is now S’:
Again, this formula accounts for the diffraction by the rightmost barrier and for the ground effects on both sides of the barrier.
See the Matlab script for the details of the computations.
A_{boundary,2,i} = A_{dif,H,i} = %DELTA_{dif,S'R,i} + %DELTA_{ground,S'O,i} + %DELTA_{ground,italic "OR",i}

---
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
To compute Aboundary,2,i , use the same procedure as in tutorial of week 6 with the barrier, except that the source position is now S’:
Again, this formula accounts for the diffraction by the rightmost barrier and for the ground effects on both sides of the barrier.
See the Matlab script for the details of the computations.
A_{boundary,2,i} = A_{dif,H,i} = %DELTA_{dif,S'R,i} + %DELTA_{ground,S'O,i} + %DELTA_{ground,italic "OR",i}

---
e) Compute the A-weighted sound level Lp,A at the receiver position in the situation of figure 3, that means with the two barriers in homogeneous conditions. Assume the absorption coefficient αr,i from the barrier is equal to 0. Make use of Figure 4.
You can now compute Lp,n=2,i
The total sound level (per octave band) is then the logarithmic sum of all paths:
And, finally, you need to apply the A correction.
The total sound level is now 54.0 dB(A); with only one barrier, the level was 48.6 dB(A) !
This is because the sound from the road reflects on the second barrier, which creates a new sound path, which is not good for the quietness of the residential area on the right of the road.

---
f) How much is Lp,A reduced when the faces of the barriers have an absorption coefficient α = 0.9 for all frequencies?
With this absorption coefficient, the sound power of the image source is reduced by 10 dB. The sound level associated with path 2 then needs to be recalculated, and the new A-weighted total sound level is found to be 49.6 dB(A), corresponding to a reduction of about 5 dB(A) in the residential area (which is good, although the level is still higher than without the second barrier).
Bottom line: a noise barrier redirects the sound but does not absorb it. It can decrease the noise in an area while increasing the noise somewhere else. Using absorbing materials on or next to the barriers can help with sound absorption.