## Slide 1: Architectural Acoustics
Jieun Yang (j.yang3@tue.nl) Assistant professor, Building Acoustics group
Week 5: Building Acoustics
Lecture B.2

## Slide 2: Introduction: Building Acoustics
Sound waves in isotropic solids
Building Acoustics
Sound reduction through multiple surfaces and ducts
Flanking sound transmission
Lecture B.1 (Chapter 10)
Lecture B.2 (Chapter 14)
Lecture B.3 (Vigran Chapter 9)

## Slide 3: Chapter 14. Building Acoustics
Air-borne sound vs. Structure-borne sound
Air  solid (wall)  air
Solid (floor)  air
Wall
Source room
Receiving room
Floor/Ceiling
Source room
Receiving room
Air-borne
Structure-borne
Air-borne
Air-borne
Air-borne
Structure-borne
Structure-borne

## Slide 4: Chapter 14. Building Acoustics
Air-borne sound insulation
Characterization & Measurements
Single leaf partition
Double leaf partition
Incident sound
Transmitted sound
Incident sound
Transmitted sound

## Slide 5: 14.1 Characterization and measurement
Sound reduction index
Sound reduction index
(or sound transmission loss, transmission loss)
[dB]
Source
Source room
Receiver room
(S = surface area of the partition)
For measurements we prefer to use
[dB]
S
 will be continued in slide 6

## Slide 6: 14.1 Characterization and measurement
Measurements
Two reverberation rooms
Sound source
Microphone
Microphone
Reverberation room in acoustic lab (Echo)
Requires diffuse sound field
Direction and phase of sound waves can be regarded as random
Acoustic energy density w [J/m3] is a constant
Concrete walls
Acoustic diffusers
Source room
Receiver room


## Slide 7: 14.1 Characterization and measurement
Transmitted power in receiver room:
A: Equivalent absorption area of the receiving room
(Obtained from the measured reverberation time)
Temporal change of energy content
= power radiated by wall - power absorbed by boundaries
Chapter 13.4

S: the surface area of the partition
Incident power (source room):
Measurements
This leads to
Sound reduction index of a partition measured by two reverberation room method
,
Sound reduction index
Substitute into


## Slide 8: 14.1 Characterization and measurement
Field measurements
https://ateliercrescendo.ac/laboratory-or-on-site-sound-insulation-rating/
Direct transmission + Flanking transmission

## Slide 9: 14.3 Single leaf partitions
Incident sound
Transmitted sound
Single leaf partition
(very thin plate)

## Slide 10: 14.3 Single leaf partitions
Incident wave
Reflected wave
Transmitted
wave
Incident, reflected, and transmitted pressures
Pressures on both sides of the partition (at )
Displacement component of the partition (at )
Sound waves around a single leaf partition
Partition thickness , mass density
Very thin partition, no damping
Plane wave incidence with incidence angle θ
x
y

## Slide 11: 14.3 Single leaf partitions
Bending wave equation,
imposed force is pressure difference over wall (at )
Incident wave
Reflected wave
Transmitted
wave
Sound waves around a single leaf partition

Expressing the displacement of the wall by its velocity
(1)
in lecture B.1
: specific mass of partition
: Bending stiffness of partition
x
y

## Slide 12: 14.3 Single leaf partitions
Sound waves around a single leaf partition
Incident wave
Reflected wave
Transmitted
wave
Normal velocity continuity (at )
Similarly,
,

(2)
(2’)
(3)
To calculate sound reduction index,
x
y

## Slide 13: 14.3 Single leaf partitions
Incident wave
Reflected wave
Transmitted
wave
Equations (1), (2’), and (3)

Sound reduction index of single leaf partitions
Sound reduction index
(1):
(2’):
(3):
Substitute (2’) and (3) to (1)

## Slide 14: 14.3 Single leaf partitions
Approximately 6 dB increase for doubling frequency (+ 6 dB/octave)
(i) For or normal incidence ()
Sound reduction index characteristic
Normal incidence
+ 6 dB/octave
increasing
Approximately 6 dB increase for doubling mass  Mass law
Mass controlled region

## Slide 15: 14.3 Single leaf partitions
(ii) For ,
Sound reduction index characteristic
Normal incidence
Total transmission (no sound insulation)!
Coincidence frequencies
= 0
Coincidence frequency
Pressure maxima and minima are spatially matched  energy is easily transmitted from the air into the partition and vice versa
Dependent on the incidence angle (c.f., )
Critical frequency () is lowest coincidence frequency
“projection” of the wavenumber (or the wavelength) in air corresponds to the bending wavenumber of the wall
Critical frequency
: coincidence condition

## Slide 16: 14.3 Single leaf partitions
(iii) For
Sound reduction index characteristic
+ 18 dB/octave
Normal incidence
Approximately 18 dB increase for doubling frequency (+ 18 dB/octave)
Stiffness-controlled region

## Slide 17: 14.3 Single leaf partitions
Sound reduction index characteristic
More on coincidence frequency
Frequency
Wave speed
Speed of sound c
Speed of bending waves
Critical frequency
Coincidence frequency
x
x
https://apmr.matelys.com/BasicsAcoustics/CoincidenceFrequency/index.html
Below
At
Above
Bending waves
Sound waves
: coincidence condition

## Slide 18: 14.3 Single leaf partitions
We also should include
Random incident sound waves
Damping of bending waves
Finite dimensions of partitions
Sound reduction index of single leaf partitions – Real situations
General form of the diffuse field TL curve
+6 dB/octave
~3dB
Dip around
Fahy, Sound and Structural Vibration 2nd Ed., 2007
Long, Architectural Acoustics 2nd Ed., 2014
https://apmr.matelys.com/BasicsAcoustics/TL/index.html

## Slide 19: 14.4 Double leaf partitions
https://images.app.goo.gl/y1mcDM6JeJrU75pc9
Incident sound
Transmitted sound
Double leaf partition
Single glazed
Double glazed
Triple glazed

## Slide 20: 14.4 Double leaf partitions
Sound reduction index of double leaf partitions
Specific mass of partition 1
Specific mass of partition 2
For normally incident plane waves
where
(: characteristic impedance of air)
air

## Slide 21: 14.4 Double leaf partitions
Sound reduction index characteristic
(i) At very low frequencies,
12 dB/octave
(ii) At
imaginary part of

6 dB increase per octave
mass-air-mass
resonance
air
Single partition at low frequencies
Follows mass law ( total mass of the system)
 Resonance of the system, Both layers vibrate in equal phases
: mass-air-mass resonance

## Slide 22: 14.4 Double leaf partitions
Sound reduction index characteristic
18 dB increase per octave
(iii) Beyond resonance frequency,
The thickness of the air gap between the layers becomes comparable to the acoustical wavelength  cannot be regarded as lumped elements anymore
(iv) At very high frequencies,
12 dB/octave
Sharp dips on the curves at
Cavity resonances
~ 12 dB increase per octave
First cavity resonance

## Slide 23: 14.4 Double leaf partitions
12 dB/octave
mass-air-mass
resonance
First cavity resonance
air
+ 6 dB/octave
Mass-controlled
increasing
+ 18 dB/octave
Coincidence frequencies
Stiffness-controlled
Normal incidence
Single leaf partition
Double leaf partition

## Slide 24: 14.4 Double leaf partitions
We also should include
Damping of bending waves
Finite dimensions of partitions (mechanical coupling of layers)
Random incident sound waves
(Vigran, Building Acoustics)
12 mm chipboards with a cavity of depth 95 mm filled with mineral wool
Sound reduction index of double leaf partitions – Real situations
Top view
Installation method to prevent mechanical coupling

## Slide 25: Summary
Building Acoustics – Airborne sound insulation
Lecture B.2 (Chapter 14)
Sound reduction index
Sound reduction index by measurement
Single leaf partition & Double leaf partition
+ 6 dB/octave
Mass-controlled
increasing
+ 18 dB/octave
Coincidence frequencies
Stiffness-controlled
Normal incidence
mass-air-mass
resonance
First cavity resonance
12 dB/octave
air

## Slide 26
& for all f under normal incidence