## Slide 1: The Science of Sound
Module 1 – Physics of Sound
Tanmayee Pathre (t.u.pathre@tue.nl)
lectures adapted from the textbook Building Acoustics Group
Pictures from Google

## Slide 2: Contents
Fundamentals of sound
What is sound
Sound source
Physical quantities
Vibrating systems
Mass-spring system
Simple harmonic motion
Waves
Properties
Progressive Waves, Impulsive waves
Wave phenomena
Resonance
Definition
Standing wave in pipes and string
Acoustic Impedance

## Slide 3: Learning Objectives
Understand the concept of wave and the relationship between wave speed, wavelength and frequency
Understand the concept of harmonic motion and resonance frequency of a spring-mass-damper system
Understand the principles of sound reflection, refraction, diffraction, interference and Doppler effect
Be able to perform basic calculations regarding quantities such as resonance frequencies, acoustic impedance or acoustic energy
Be able to perform basic calculations regarding the design of acoustic resonators

## Slide 4: Fundamentals of sound

## Slide 5: Fundamentals of Sound
What is sound?
An auditory sensation in the ear
The disturbance in a medium that can cause this sensation
Sound wave
Longitudinal wave
(NOT) Transverse wave
ISVR – University of Southampton http://resource.isvr.soton.ac.uk/spcg/tutorial/tutorial/Tutorial_files/Web-basics-nature.htm
Longitudinal wave
Transverse wave

## Slide 6: Fundamentals of Sound
Sound source
https://www.youtube.com/watch?v=ycRVAcZC5R4
Vibrating bodies – Striking drum kit
Changing airflow – Talking or singing
Time-dependent heat sources – Explosion
Supersonic flow – Shock wave

## Slide 7: Fundamentals of Sound
Sound source
Wanted
Unwanted
“Noise”
Sound source
Medium
Listener

## Slide 8: Fundamentals of Sound
Physical quantities
Physical quantities | Mathematical expression | Units (SI)
Speed | v = | m/s
Acceleration | a = | m/s^2
Acceleration (in terms of Force and mass) | a = | m/s^2
Pressure | p = | N/m^2
Work | W = Force[N] *Displacement[m] | J or N·m
Potential Energy | P.E. = Mass[kg]*g[m/s^2]*Height above the floor/earth[m] | J or N·m
Kinetic Energy | K.E. = *Mass[kg]*Velocity^2[m/’s]^2 | J or N·m
Power | P = | W or J/s or N·m/s
Physical quantities | Mathematical expression | Units (SI)
Speed |  | m/s
Acceleration |  | m/s^2
Acceleration (in terms of Force and mass) |  | m/s^2
Pressure |  | N/m^2
Work | W = Force[N] *Displacement[m] | J or N·m
Potential Energy | P.E. = Mass[kg]*g[m/s^2]*Height above the floor/earth[m] | J or N·m
Kinetic Energy |  | J or N·m
Power |  | W or J/s or N·m/s
g = acceleration due to gravity = 9.8m/s^2 for earth
Notes: Power – The rate at which the work is done

## Slide 9: Vibrating systems

## Slide 10: Vibrating system
motion of vibrating system repeats at regular time interval - the period of the vibration
A force constantly acts to restore the system toward its equilibrium position – Restoring Force
Source: The Physics Classroom

## Slide 11: Vibrating system
motion of vibrating system repeats at regular time interval - the period of the vibration
A force constantly acts to restore the system toward its equilibrium position – Restoring Force
Source: The Physics Classroom

## Slide 12: Vibrating system
Mass-spring system
spring
mass
Understanding Simple Harmonic Motion
Understanding Resonance
Source: The Physics Classroom

## Slide 13: Vibrating system
Simple Harmonic Motion
Periodic motion
Restoring force (F) is proportional to the displacement (y)
Restoring force (F) always acts in a direction to restore mass (m) in equilibrium
F = Restoring force (N)
K = spring constant (N/m)
y = displacement (m)
Equilibrium

## Slide 14: Vibrating system
Simple Harmonic Motion
Restoring Force
Frequency of vibration is number of oscillations per second (in Hz)
Frequency of vibration of a spring mass damper system is given as
f = frequency of vibration (Hz)
K = spring constant (N/m)
m = mass (Kg)
Source: The Physics Classroom

## Slide 15: Vibrating system
Energy and Damped Motion
Total Mechanical Energy of the system constantly changing from kinetic to potential to kinetic.
y = distance from equilibrium (m)
v = speed of moving mass (m/s)
m = mass (Kg)
Notes: As v goes to maximum y to zero and vice versa

## Slide 16: Vibrating system
Energy and Damped Motion
Any real vibrating system tends to lose mechanical energy as a result of friction and other loss mechanisms.
Damping - Tendency of a vibrating object to lose or to dissipate its energy over time.
A vibrating system whose amplitude decreases in this way is said to be damped, and the rate of decrease is the damping constant.
Notes: Damping as a function of time

## Slide 17: Vibrating system
Some more vibrational systems
Simple pendulum
Helmholtz resonator
l = length of string (m)
g = acceleration due to gravity (m/s2)
l = length of neck (m)
A = area of the neck (m2)
V = Volume of the resonator (m3)
v = Speed of sound (approx. 344 m/s)
Notes: These systems also show simple harmonic montion

## Slide 18: Waves

## Slide 19: Waves
What is wave?
Disturbance in medium that travels from one position to another position
All waves (light waves, sound waves, surface waves)
Transport energy
Exhibit phenomena :
Reflection
Refraction
Interference
Diffraction

## Slide 20: Waves
Wave properties
Source: Khan Academy
v = speed of sound (m/s)
f = frequency (Hz)
wavelength (m)

## Slide 21: Waves
http://www.animations.physics.unsw.edu.au/
Progressive wave
Travel continuously in medium in same direction
Longitudinal waves in solid :
Transverse waves on a string:
= Elastic modulus (N)
= density of solid (Kg/m3)
= Tension of the string (Force) (N)
= mass per unit length (Kg/m)
Notes: Longitudinal and Transverse waves are types of Progressive waves.

## Slide 22: Impulse/ Impulsive wave
The impulse will travel at the wave speed v and will retain its shape fairly well as it moves down the rope
Waves
Fixed end : reversal of phase of reflected wave
Free end : No phase reversal

## Slide 23: Waves
Superposition and interference
Wave pulses on rope or string obey principle of superposition - the
displacement at any point is the sum of the displacements due to each pulse by itself.
Pulses in same direction
Pulses in different direction
Pulses with different shapes

## Slide 24: Waves
Standing wave or Stationary Wave
Combination of two waves
Moving in opposite direction
Each wave has same amplitude and frequency
A standing wave (black) depicted as the sum of two propagating waves traveling in opposite directions (red and blue).

## Slide 25: Waves
Standing wave or Stationary Wave
Amplitude displacement minimum - Node
Amplitude displacement maximum - Antinode
Source: ProDuckTheives

## Slide 26: Sound Waves
Sound wave
Longitudinal wave
Travels in solid, liquid, gas

## Slide 27: Sound Waves
Wave Propagation in two dimensions
Example: Water waves
Source: Resonance BlogSpot

## Slide 28: Sound Waves
Wave Propagation in three dimensions
Example: Sound waves or light waves
Single loudspeaker - Point source
Column of loudspeakers - Cylindrical source
Notes: Different types of sources radiate different kinds of patterns. A point source or a source
that is spherically symmetric radiates spherical waves. A line source or a source with cylindrical
symmetry radiates cylindrical waves. A large flat source radiates plane waves. Real
sound sources are never true point sources, line sources, or flat sources, however; what we
may have in real life are sources that approximate one of these geometries.

## Slide 29: Sound Waves
Reflection
Sound waves reflected back to the source when encountered by a barrier
Principle - Image source
Example : Whisper gallery
Notes: S prime at the same distance from S, Reflections from a curved barrier

## Slide 30: Sound Waves
Refraction
Change in speed of sound
Light wave passes from one medium to another
Sound waves in the atmosphere when
temperature varies with height
Sound traveling against the wind
Notes: Pg 53

## Slide 31: Sound Waves
Diffraction
Bending of waves around the corners of obstacle or through an aperture
Size of the opening in relation to the wavelength that determines the amount of diffraction.
Source: Wave Behaviour Raft

## Slide 32: Sound Waves
Interference
Two traveling in the same medium will interfere with each other
Constructive or Destructive Interference
Representation via water wave
https://www.youtube.com/watch?v=D7aftTF--5w

## Slide 33: Sound Waves
Doppler effect
Apparent shift in frequency when either the sound source or observer is in motion
Example:
Source: Wikipedia and Charly Whisky
Apparent frequency when Source at rest, observer in motion:
Apparent frequency when Observer at rest, source in motion:
= frequency of the source (Hz)
= speed of sound
= frequency (Hz)

## Slide 34: Resonance

## Slide 35: Resonance
Resonance
Resonance occurs when one object vibrating at the same natural frequency of a second object forces the second object into vibrational motion.
Example: Breaking a wineglass – Glass breaks when a applied frequency matches natural frequency of wineglass
Source: YouTube

## Slide 36: Resonance
Resonance – Mass Spring damper system
= Natural frequency of the mass spring system
= Frequency of crankshaft
When driving frequency, the natural frequency of the system, resonance occurs
Notes: Let the crankshaft revolve at a frequency f and let the natural frequency of the mass-spring system be f0. If f is varied slowly, the
amplitude A of the mass is observed to change, reaching its maximum Amax when f = f0. The mass is forced to vibrate at the frequency f of the crank, but when f matches f0, the
natural frequency of the system, resonance occurs. At resonance the maximum transfer of
energy occurs, and the amplitude builds up to a value Amax determined by the friction in
the system. The graph of amplitude A as a function of frequency f , shown in Fig. 4.2,
is nearly symmetrical around its peak, with a width f often called the linewidth. The
linewidth is usually measured at an amplitude of 71% of Amax(Amax/
√
2).

## Slide 37: Resonance
Standing wave on a String
Resonance also happens in standing waves.
Driving the string at a specific frequency will cause it to “sing”/resonate.
Each frequency has a corresponding mode shape.
String: https://www.youtube.com/watch?v=oZ38Y0K8e-Y Plate: https://www.youtube.com/watch?v=wvJAgrUBF4w
Fundamental (1st harmonic)
1st overtone (2nd harmonic)
2nd overtone (3rd harmonic)
(n-1)th overtone (n-th harmonic)
Notes: If a string is driven at the frequency of one of its natural modes, resonance can occur. Driving force can be tuning fork, electromagnet, violin bow

## Slide 38: Resonance
Open and Closed Pipes
Resonance also occurs in Pipes
Modes of vibration in open pipes.
Modes of vibration in closed pipes.
Source: AllaboutCircuits
Notes: Modes of vibration or resonances of an open pipe. At the open ends the pressure is equal to atmospheric
pressure. The resulting modes include both odd-numbered and even-numbered harmonics. Minimum displacement occurs at
the nodes denoted by N.
Modes of vibration or resonances of a closed pipe. At the closed end, the air motion is minimum but the
pressure is maximum. The resulting modes include odd-numbered harmonics only. Minimum displacement occurs at the
nodes denoted by N.
N is the node.

## Slide 39: Resonance
Resonance – Other examples
Ear Canal
Vocal Tract
Source: ResearchGate - Development of the human auditory system (2012), Bethroars

## Slide 40: Resonance
Acoustic Impedance
Defined as the ratio of sound pressure p to volume velocity U
Measured in acoustic ohms.
Acoustic Impedance of wind instruments – determines acoustic response and large influence on sound produced
= Sound pressure
= Volume velocity

## Slide 41: Resonance
Helmholtz Resonator – Applications

## Slide 42: Wrap up
Take away message
Fundamentals of Sounds
Sound sources and processes of sound generation
Physical quantities provide information to analysis motion of an object
Vibrating Systems
Simple harmonic motion – Restoring force directly proportion to displacement
Damping - Loss of mechanical energy over time
Waves
Transport energy
Wave behavior encountered in various phenomena
Resonance
Driving frequency of one object equal to natural frequency of second object
Observed in string, pipes

## Slide 43: Questions?
Pictures from Google

## Slide 44: Thank you!
Pictures from Google