## Slide 1: The Science of Sound
Module 2
Lecture 3 – Sound Perception
Tanmayee Pathre (t.u.pathre@tue.nl)
lectures adapted from the textbook Building Acoustics Group
Pictures from Google

## Slide 2: Contents
Range of Hearing
Anatomy of ear
Spatial Hearing
Perceptual correlates of sound –
Pitch
Timbre
Loudness
The Decibel Scale
Masking and Critical Bands

## Slide 3: Learning Objectives
Parameters of range of hearing system
Some basic anatomy and physiology of human hearing system
Spatial hearing – cues for sound localization
Understanding and experiencing the perceptual quantities – Loudness, Pitch and Timbre
Concept of Masking and Critical Bands

## Slide 4: Range of Hearing

## Slide 5: Range of hearing
Human Auditory System – A fascinating system
Response to a range of pressures, frequencies and intensities
Audible frequency range for humans – 20 Hz to 20,000 Hz.
Frequency selectivity
Pick solo instrument from an orchestra
Hear your friend in a room full of people

## Slide 6: Range of hearing
Ear insensitive to low frequencies such as 100 Hz
Highly sensitive between frequency range 2000 Hz to 5000 Hz.
Notes: Review question in Week

## Slide 7: Anatomy of human ear

## Slide 8: Anatomy of ear
Acoustical
Mechanical
Electrical

## Slide 9: Anatomy of ear

## Slide 10: Anatomy of Ear
The Outer ear
Pinna
Irregular grooves and ridges – Why?
Auditory canal or Ear canal
Almost like an open-close pipe
Source: External
Notes: Why do we need an outer ear? What if we did not have an outer ear?

## Slide 11: Anatomy of Ear
The Outer ear
Pinna
  Protection to sensitive inner ear
  Acts as funnel – collecting sound
  Irregular shape of pinna  Sound localization  Provides physical cues for locations
Auditory canal or Ear canal
Ear canal resonance  Boosts hearing sensitivity in the range 2000 Hz to 5000 Hz.

## Slide 12: Anatomy of Ear – Middle Ear

## Slide 13: Anatomy of Ear – Middle Ear
The Middle ear
Tympanic membrane/Ear drum
Three bones – Ossicles
Malles (25 mg)
Incus (30 mg)
Stapes (3 mg)
Source: Funkids
Source: www.chadruffinmd.com/endoscopic-ear-surgery

## Slide 14: Anatomy of Ear – Middle Ear
The Middle ear - Functions
Impedance Transformer  Transmission of tympanic membrane (ear drum) movements to the fluid which fills the cochlea without significant loss of energy
Protects the hearing system from loud sounds – Acoustic Reflex
Pressure equalization
Source: Earplanes

## Slide 15: Anatomy of Ear – Middle Ear
The Middle ear – Impedance Transformer
Source: Acoustics and Psychoacoustics, Book
Act as a lever which changes pressure from eardrum to the oval window on inner ear.
Lever effect of malleus and incus
Area difference between tympanic membrane

## Slide 16: Anatomy of Ear – Middle Ear
The Middle ear – Acoustic Reflex
Ear muscles automatically contract in response to sound levels greater than 75 dB SPL
Contraction stiffens the ossicular chain and thus impedance increases.
Reduction in efficiency with which vibrations are transmitted from ear drum to inner ear

## Slide 17: Anatomy of Ear – Middle Ear
The Middle ear – Pressure equalization
Ear drum makes air tight seal between middle and outer parts of ear  pressure equalization
Eustachian Tube – Connects middle ear cavity to nasopharynx
Ears “pop” when Eustachian tube opens
Change in air-pressure during landing and take off (change in altitude)

## Slide 18: Anatomy of Ear – Inner Ear

## Slide 19: Anatomy of Ear – Inner Ear
The Inner ear
Semi-circular canals – Body’s horizontal and vertical detectors  Sense of balance
Cochlea – Bony snail like structure filled with fluid  Related to hearing
Source: Hyperphysics
Source: Wikipedia
base
apex

## Slide 20: Anatomy of Ear – Inner Ear
The Inner ear - Cochlea
Converts mechanical vibrations into neural impulses that can be encoded by the brain
Source: C.J.Plack

## Slide 21: Anatomy of Ear – Inner Ear
The Inner ear
Source: C.J.Plack
Organ of corti – Seat of hearing
Consists of Hair cells. These hair cells are attached to nerve fibres.
Outer hair cells – 12,000 in a single row  Amplification of sound
Inner hair cells – 4000 in a single row Transmitting signals to nerve fibers

## Slide 22: Anatomy of Ear – Inner Ear
The Inner ear
Each hair cell has many hairs or stereocilia.
Stereocilia are bent when basiliar membrane responds to sound
Bending of stereocilia stimulates hair cells, which in turn excites neurons in auditory nerve 
Source: Cochlear Mechnanics
Basilar membrane
Auditory nerve
Outer hair cells
Inner hair cells
Stereocilia
Tectoral membrane

## Slide 23: Anatomy of Ear – Inner Ear
Source: YouTube
The Inner ear – The Dancing Hair cell
https://www.youtube.com/watch?v=wKEhjpqpzCE

## Slide 24: Anatomy of Ear – Inner Ear
The Inner ear – Basilar membrane
Source: C.J.Plack
Basilar Membrane – frequency analyzer
Narrow and thin at the base, wider and thicker at the apex.
Response to high frequencies at the base, low frequencies at the apex

## Slide 25: Anatomy of Ear – Inner Ear
The Inner ear
Stapes vibrate against the oval window, hydraulic waves transmitted via scala vestibuli.
Pressure waves travel via the cochlear fluid towards the round window causing ripples on the membrane

## Slide 26: Anatomy of Ear – Inner Ear
The Inner ear – Basilar membrane
Travelling wave on the entire membrane
High frequencies create ripples at the base, low frequencies create ripples at the apex.
Source: C.J.Plack

## Slide 27
https://youtu.be/46aNGGNPm7s
Sound propagation inside the ear – in a nutshell

## Slide 28: Spatial Hearing

## Slide 29: Spatial Hearing
Binaural hearing  Sound localization
Enhancement of ability to sense the direction of sound source
Physical basis for these cues
  Distance between ears (approximately 18 cm)
  The head in between the ears (acoustic shadow)
  Spectral filtering by outer ear (pinna)
Basic cues
  Interaural differences in time (ITD)
  Interaural differences in level (ILD)
Binaural Hearing

## Slide 30: Spatial Hearing
Difference between arrival time between two ears
Low frequency components are present – ITD most important cue for sound source localization
Interaural Time Differences
Where c is the speed of sound

## Slide 31: Spatial Hearing
Difference in sound level between two ears
ILD arise because of Head-shadow effect – sound needs to bend around the head
Low frequencies diffract more than high frequencies, so the level cue is
most salient at high frequencies.
Interaural Level Differences

## Slide 32: Spatial Hearing
Which cue is dominant? – Duplex Theory (Lord Rayleigh, 1907)
  ITDs are used at low frequencies
  ILDs are used at high frequencies
  Transition region around 2 kHz

## Slide 33: Spatial Hearing
  Spectral filtering by outer ear (pinna)
  At frequencies above 5000 Hz, Pinna helps in sound localization.
  Particularly from sound coming from front and back

## Slide 34: Spatial Hearing
  Applications
Surround Sound: 5.1, 7.1, 22.2
Higher-Order-Ambisonics (HOA)
Wave Field Synthesis (WFS)
3D Sound - Immersive Audio – Video games, Virtual Reality

## Slide 35: Spatial Hearing
  Listening Demonstration
https://www.youtube.com/watch?v=IUDTlvagjJA

## Slide 36: Pitch

## Slide 37: Pitch
Source: Plomp CD Perceptual Audio Demonstrations
Pitch
Pitch is defined as that attribute of auditory perception which allows to order sounds on a scale from low to high. (ANSI definition)
Pitch and frequency are not the same not even for a pure tone (sinusoid)
  Perceived pitch of pure tones can vary with level
  Sound with very different spectral composition can induce the same pitch percept (example: musical instruments)

## Slide 38: Pitch
Source: Perceptual Audio Demonstrations
Listening Demonstration – Pitch
  In complex tones, the fundamental frequency determines the pitch, even if this component is absent in the complex.
Three demonstrations were created to illustrate pitch as an auditory phenomenon relating to frequency.
This demonstration investigates how pitch is perceived in time.
Each track plays time bursts of sound.
Initially the tones will sound like pops or blips, but as the tones increase in time duration they will begin to have pitch. Each demonstration uses a different frequency of tone.
Track 1
Track 2
Track 3

## Slide 39: Timbre

## Slide 40: Timbre
Timbre
Timbre – Tone colour or sound quality
Auditory percept which allows to judge that two stationary sounds which have equal loudness, pitch, duration, and spatial direction sound different
Timbre is thus mainly dependent on the spectral composition of a sound,  amplitude spectrum, but also phase of components can contribute to timbre
Musical instruments have different timbres – flute does not sound same as saxophone!!!
Timbre also is the basis for distinction between different vowels in speech

## Slide 41: Timbre
Source: Plomp CD and Perceptual Audio Demonstrations
Listening Demonstration – Timbre
Track 1
Track 2
Demonstration to understand differences in Timbre

## Slide 42: The Decibel Scale

## Slide 43: Range of hearing
  The Decibel (dB) scale
  Enormous range of pressures and intensities  Huge numbers
  Specify intensity in logarithmic units – decibels (dB)
Notes: Review question in Week

## Slide 44: Sound Level
Source: C.J.Plack
Notes: Review question in Week

## Slide 45: Sound Level
  The Decibel (dB) – A little more
  dB – Logarithmic way of describing a ratio
  The ratio may be of power (P), sound pressure(p), intensity(I) or voltage.
  The factor of 10 which puts the ‘deci’ in decibel: level difference in bels (named after Alexander Graham Bell).
Notes: Review question in Week

## Slide 46: Sound Level
  The Decibel (dB)
  Sound level – Power
  Sound level – Intensity
  Sound level - Pressure
Where Po = 10-12 W
Where Io = 10-12 W/m2
Where po = 2x10-5 N/m2
Notes: Review question in Week

## Slide 47: Sound Level
Source: SUVA CD track 18
  Ticks of a clock (30 dB)
  Painting (40 dB)
  Cutting paper (50 dB)
  Washing hands (60 dB)
  Toilett flush (70 dB)
  Vacuum cleaner (noisy model, 80 dB)
  Stone drill (100 dB)
Listening demonstration – Examples

## Slide 48: Loudness
Source: SUVA CD track 14
Listening Demonstration – Level
Level differences of 0 tot +10 dB between successive sounds
Relative levels of individual sounds
Try to find out which difference leads to a perceivable difference
  0 dB, +1 dB, 0 dB, +3 dB, 0 dB, +6 dB, 0 dB,+10 dB, 0 dB

## Slide 49: Loudness
Source: Wikipedia
Measuring Sound Pressure Level
  Use of Sound Level Meter
  Provided with Different Weightings
Source: abcgeluid

## Slide 50: Different Weightings of Sound
  A weighting dB (A)
  Most common weighting. dB(A) roughly corresponds to the inverse of the 40 dB (at 1 kHz) equal-loudness curve for the human ear.
  B – Weighting dB (B)
  Rarely used
  C Weighting dB (C)
  Suitable for subjective measurements only for moderate to high sound levels
Notes: Negative gain means the output is inverted from the input. For the gain to be negative, the output would have to go down when the input goes up, which is clearly not happening in your case.

## Slide 51: Loudness

## Slide 52: Sound Level
  Loudness
Loudness – perceptual quantity primarily related to sound intensity
Categorization of sounds by variation in intensity
Variation across time and frequency
Notes: Review question in Week

## Slide 53: Range of hearing
Source: StudioTone
Each curve represents the levels and frequencies of pure tones of equal loudness, measured relative to a 1000-Hz pure tone.
A pure tone corresponding to a point on a given curve will sound as loud as a pure tone at any other point on the same
curve. The level of the 1000-Hz tone for each curve (in dB SPL) is shown on the figure above each loudness contour.
Fletcher-Munson Curves Equal Loudness contours

## Slide 54: Masking and Critical Bands
Listening Demonstration – Loudness
Source: Perceptual Audio Demonstrations
Demonstration shows that the perceived loudness of tones varies at equal sound intensity.

## Slide 55: Masking and Critical Bands

## Slide 56: Masking and Critical Bands
Masking
Masking is the process by which the detection threshold of a sound (called ‘the signal’) is increased by the presence of another sound (called ‘the masker’).
Masking describes the effect that a stimulus, which is clearly perceivable (audible) when presented in isolation, becomes unperceivable (inaudible) in the presence of another stimulus

## Slide 57: Masking and Critical Bands
masker
test signal
frequency
Measure threshold of detectability of a tone masked by bandpass noise centred spectrally around the tone
Measure thresholds as a function of masker bandwidth
bandwidth
SPL
masked threshold
*
Fletcher Experiment, Critical Band Estimation

## Slide 58: Masking and Critical Bands
masker
test signal
frequency
Measure threshold of detectability of a tone masked by bandpass noise centred spectrally around the tone
Measure thresholds as a function of masker bandwidth
bandwidth
SPL
masked threshold
*
*
Fletcher Experiment, Critical Band Estimation

## Slide 59: Masking and Critical Bands
masker
test signal
frequency
Measure threshold of detectability of a tone masked by bandpass noise centred spectrally around the tone
Measure thresholds as a function of masker bandwidth
bandwidth
SPL
masked threshold
*
*
*
Fletcher Experiment, Critical Band Estimation

## Slide 60: Masking and Critical Bands
masker
test signal
frequency
Measure threshold of detectability of a tone masked by bandpass noise centred spectrally around the tone
Measure thresholds as a function of masker bandwidth
bandwidth
SPL
masked threshold
*
*
*
*
Fletcher Experiment, Critical Band Estimation

## Slide 61: Masking and Critical Bands
masker
test signal
frequency
Measure threshold of detectability of a tone masked by bandpass noise centred spectrally around the tone
Measure thresholds as a function of masker bandwidth
bandwidth
SPL
masked threshold
*
*
*
*
*
critical bandwidth
Fletcher Experiment, Critical Band Estimation

## Slide 62: Masking and Critical Bands
Few Findings from Masking Experiment
Pure tones that are close together in frequency mask each other better than those widely separated.
Pure tones also mask higher frequencies better than lower frequencies.
Tone of greater intensity masks a broader ranger of tones than a tone of less intensity

## Slide 63: Masking and Critical Bands
Listening Demonstration – Masking
Pure tones that are close together in frequency mask each other better than those widely separated.
A single tone is played, followed by the same tone and a higher frequency tone. The higher frequency tone is reduced in intensity first by 12 dB, then by steps of 5 dB. The sequence above is repeated twice. The second time the frequency separation between the tones is increased
Pure tones also mask higher frequencies better than lower frequencies.
High Frequencies masked 
Low frequencies are masked 
Source: Perceptual Audio Demonstrations

## Slide 64
Listening Demonstration – Masking
Masking and Critical Bands
Tone of greater intensity masks a broader ranger of tones than a tone of less intensity
A single tone is played, followed by the same tone and a higher frequency tone. The higher frequency tone is reduced in intensity first by 10 dB, then by steps of 3 dB. The sequence above is repeated twice, the second time increasing the intensity of the single tone by 28 dB.
Source: Perceptual Audio Demonstrations

## Slide 65: Wrap up
Take away message
Overview of Human Auditory system
Spatial Hearing  Sound Localization
Loudness, Pitch and Timbre – Perceptual Correlates of sound
Decibel Scale  Ratio  Pressure, Intensity, Power
Masking and Critical Band  Estimation of Auditory filter

## Slide 66: Questions?
Pictures from Google